## Slide 1
A novel methodology for robustness analysis of QCA circuits
Dayane Alfenas Reis
dayanealf@gmail.com
SBCCI 2015 – August 31st to September 4th
Salvador, Bahia - Brazil
Frank Sill Torres
franksill@ufmg.br

## Slide 2
Agenda
Motivation
Background
Methodology
Simulations and results
Conclusions

## Slide 3
Motivation - CMOS Limits about to be reached
Nano technologies as QCA have been emerging as possible CMOS successors.
Scaling
High performance requirements
Integration density
Leakage
High power consumption
Notes: High power dissipation (OFF leakage currents due to quantum effects) comes with scaling.

## Slide 4
Background – Quantum-dot Cellular Automata (QCA)
QCA: A new computation paradigm.
QCA cell (basic unit)
Polarization +1
Logic state 1
Polarization -1
Logic state 0
QCA wire
Notes: QCA: computation paradigm whose working principle is based on Coulomb interactions between electrons.

## Slide 5
Background – Quantum-dot Cellular Automata (QCA)
IN1
FIXED
IN2
OUT
IN2
IN1
IN3
OUT
IN1
FIXED
IN2
OUT
Majority gate
OR
AND
Any logic can be created.
More complex circuits feasible.
Inverter
IN
OUT

## Slide 6
Background – Quantum-dot Cellular Automata (QCA)
QCA Pros
Very high theoretical speeds achieved (within THz range);
Low power consumption (information is transported with no electric current flow);
Small dimensions (a molecular QCA cell should be 2x2 nm).
QCA Cons
Extremely difficult physical implementation.

## Slide 7
Background – Defects and Errors in QCA circuits
QCA Defects Modeling
Defects: flaws of the cells of a circuit.
IN2
IN1
IN3
OUT
IN2
IN1
IN3
OUT
IN2
IN1
IN3
OUT
IN2
IN1
IN3
OUT
Dopant
Dislocation
Vacancy
Interstitial
Affect directly the interaction between cells.

## Slide 8
Methodology – Fault Simulation Flow
A new methodology for error exploration in QCA circuits which aims to be:
Flexible
Parameter-based approach
Operation under different conditions can be verified;
Extensive
Four classes of defects + Three probability models
Easy to interpret and visualize the results
Error-free simulations calculation (%)
Innovative
Heat map

## Slide 9
Methodology – Fault Simulation Flow
  Circuit selection
  Parameters choice
Initial procedures
  Error-free reference simulation
  Defect insertion
  Fault simulation
  Comparison (Error-free x defective)
Intermediate procedures
  Result analysis
  Error-free simulations percent calculation
  Design heat map
Final procedures
Repeat for all iterations
After all iterations

## Slide 10
A visual resource for results analysis
Colors used
Example
Methodology – Heat map
Map the defective cells leading the outputs to an error.
75-99%
50-75%
Given an error event, these cells have ________ of probability to be defective.
Pink cells are more likely to cause defects
Yellow cells are majorly related to defects.

## Slide 11
Methodology – Pros and Cons
Methodology Pros
Extensive defect modeling applied;
Allows flexibility for defects insertion by means of probability models;
Parameters are totally user-set;
Presents the results by a heat map of the circuit;
Provides the error-free simulations percent along all iterations.
Methodology Cons
Simulation-based: May be a computational costly approach depending on the circuit size/ complexity.
Notes: Extensive defect modeling applied: It is possible to verify the circuit behavior under several defective conditions;

## Slide 12
Simulations and results
 | INVERTER |  | 3-INPUT MAJORITY |  | FULL ADDER | 
 | INV1 | INV2 | MJ1 | MJ2 | FA1 | FA2
Vacancy | 74.6 | 86.1 | 60.6 | 30.3 | 2.8 | 16.2
Interstit. | 97.4 | 99.9 | 94.3 | 87.9 | 54.9 | 76.0
Dopant | 83.7 | 88.6 | 75.8 | 31.1 | 3.7 | 26.2
Dislocat. | 88.6 | 93.9 | 78.5 | 67.2 | 25.9 | 51.0
Error-Free Simulations (%)
Probability model = Assignable;
Number of iterations = 1.000;
Probability value for individual defect classes = 5%;
Sample Interval = 10% and LOW/HIGH Threshold = 80%.
Notes: Extensive defect modeling applied: It is possible to verify the circuit behavior under several defective conditions;

## Slide 13
Simulations and results
Two inverter (A) and (B) for 1.000 tests under vacancy defects.
Probability model “Assignable”.

## Slide 14
Simulations and results
Reliable majority cell for 1.000 tests under dopant defects (A) and interstitial defects (B). Probability model “Assignable”.

## Slide 15
Conclusions
The new methodology presented is useful to:
  Design more reliable QCA circuits/ structures;
  Compare QCA circuits in terms of robustness;
  Verify the reliability of a QCA circuit undo different test conditions;
Simulation results proved the feasibility of the methodology.

## Slide 16
Thank you!
Questions?
See you in Belo Horizonte...
Chip on the Mountains 2016

## Slide 17
EXTRA

## Slide 18
Emerging nanotechnologies

## Slide 19
Methodology – Fault Simulation Flow
Sample interval;
HIGH/LOW thresholds;
Defect classes (As defect modeling previously exposed);
Number of iterations;
Probability model
  Sequential: P=1 for each cell of the design at sequential moments
  Assignable: Any value between 0 and 1 may be assigned as defect probability for each design cell
  Uniform: P=1/(Total of cells) for each cell of the design
Parameters list

## Slide 20
Simulations and results
Two full adder (A) and (B) for 1.000 tests under dislocation defects. Probability model “Assignable”.

## Slide 21
Simulations and results
 | INVERTER |  | 3-INPUT MAJORITY |  | FULL ADDER | 
 | INV1 | INV2 | MJ1 | MJ2 | FA1 | FA2
Vacancy | 74.6 | 86.1 | 60.6 | 30.3 | 2.8 | 16.2
Interstit. | 97.4 | 99.9 | 94.3 | 87.9 | 54.9 | 76.0
Dopant | 83.7 | 88.6 | 75.8 | 31.1 | 3.7 | 26.2
Dislocat. | 88.6 | 93.9 | 78.5 | 67.2 | 25.9 | 51.0
 | INVERTER |  | 3-INPUT MAJORITY |  | FULL ADDER | 
 | INV1 | INV2 | MJ1 | MJ2 | FA1 | FA2
Vacancy | 60.0 | 83.3 | 11.1 | 89.9 | 26.6 | 0.0
Interstit. | 96.0 | 100 | 87.8 | 98.9 | 50.9 | 83.9
Dopant | 69.0 | 80.8 | 42.2 | 85.2 | 0.0 | 37.4
Dislocat. | 88.0 | 90.8 | 61.1 | 95.2 | 77.2 | 39.0
Tables 1 and 2 - Error-Free Simulations (%)*
*Probability model=Assignable; Number of iterations=1000; Probability value for individual defect classes=5%; Sample Interval=10% and LOW/HIGH Threshold=80%.
*Probability model=Sequential; Number of iterations=10 for interstitial, dopant and dislocation defect classes. 1 for vacancy defect class. Sample Interval=10% and LOW/HIGH Threshold=80%.
Notes: Extensive defect modeling applied: It is possible to verify the circuit behavior under several defective conditions;

## Slide 22
Simulations and results
INV1 (A) and INV2 (B) for 1000 tests under vacancy defects. Probability model “Assignable”.
MJ2 for 1.000 tests under dopant defects (A) and interstitial defects (B). Probability model “Assignable”.